## Slide 1
MCT231 · BASICS OF MECHATRONICS
SpongeBob Educational Toy
A Fully Automated Mechatronic System
Ain Shams University · ICHEP · Final Submission
Ahmed Mohamed Taha · Nada Abdelhamid · Mohamed Samy Taha · Rawaa Tarig Algadi · Farida Mohamed Saeed

## Slide 2
PROJECT OVERVIEW
A fully automated SpongeBob-themed educational toy combining ball dispensing, lifting, shooting, and sorting with a closed-loop mechatronic control system. Children learn color recognition through an interactive Q&A game while the system autonomously handles every ball cycle.
🎯 Color Recognition Game
Children identify ball colors using push buttons. LCD prompts the question; buzzer gives feedback.
🔄 Closed-Loop Control
IR sensors + optical encoder provide continuous feedback for reliable, automated operation.
📡 Bluetooth GUI
HC-06 module enables wireless monitoring & control from a PC. Two Arduino Nanos via I²C.
⚙️ Full Ball Lifecycle
Dispense → Lift → Shoot → Sort → Return. Complete cycle in ≤ 2.0 seconds per ball.

## Slide 3
SYSTEM ARCHITECTURE
Dual-controller distributed design with sense–process–actuate architecture
MASTER NANO 1
🎮 Game logic & scoring
💬 LCD display (16×2 I²C)
📡 HC-06 Bluetooth GUI
🔘 Pink & Yellow buttons
🔔 Buzzer feedback
📤 Dispenser servo (IR)
I²C
SLAVE NANO 2
⬆️ Lifting servo mechanism
🏀 Shooting DC motor (L298N)
📊 Optical encoder (PID)
🔃 Sorting servo gate
📍 IR Sort Low / High
📍 IR Shooting sensor
⚡ 12V Li Battery → Buck Converter → 5V (logic / servos) | 12V direct → DC Motor + L298N

## Slide 4
HOW IT WORKS
1
Ball Dispense
Servo releases one ball when IR sensor confirms presence
2
Color Question
LCD prompts child to identify the ball's color (pink/yellow)
3
Lift Mechanism
Belt-drive servo elevates ball at 0.5 m/s to shoot rail
4
PID Shoot
N20 motor launches ball at ≈2.7 m/s, 35° angle, 30cm range
5
IR Sort
Dual IR sensors classify ball → servo gate opens left or right
6
Ball Return
Ball slides to correct bin and returns to dispenser. Cycle ≤ 2.0s

## Slide 5
ACTUATOR SIZING
Engineering calculations for three core mechanisms
Lifting Mechanism
High-Torque Servo / NEMA-17
Safety Factor ≈1.03×
Payload mass
40 g
Belt incline
55°
Peak torque
4.84 N·m
RMS torque
3.16 N·m
Peak velocity
0.5 m/s
Standard SG90 ruled out — requires DS3218 or NEMA-17 with driver
Shooting Mechanism
N20 DC Gear Motor (12V)
Safety Factor ≈1.27×
Ball mass
7.3 g (PLA)
Arm length
50 mm
Required ω
394–516 rpm
Peak torque
0.0157 N·m
RMS torque
0.0070 N·m
Safety margin 1.27×. Verify ball mass before finalizing.
Sorting Mechanism
SG90 Micro Servo
Safety Factor ≈4.9×
Rotation angle
45° sweep
Motion time
0.2 s
Peak torque
0.00365 N·m
RMS torque
0.00165 N·m
SG90 rated
0.018 N·m
Well within rating. No upgrade required.

## Slide 6
PROJECTILE MOTION CALCULATIONS
v = √[ (g · d²) / (2 · cos²(θ) · (d · tan(θ) − h)) ]
Given Parameters
Horizontal distance (d)
30.76 cm
Vertical drop (h)
12 cm
Launch angle (θ)
35°
Gravity (g)
9.81 m/s²
tan(35°)
≈ 0.700
cos(35°)
≈ 0.819
Results
2.7 m/s
Required Launch Velocity
35°
Optimal Launch Angle
1.21 m/s
RMS Velocity (continuous duty)

## Slide 7
ELECTRONICS & CONTROL
SENSORS
IR_Dispenser
Ball presence at gate
IR_Box
Arrival detection
IR_Shooting
Ball at launch cup
IR_Sort Low
Color bit LOW
IR_Sort High
Color bit HIGH
Optical Encoder
Motor speed (PID)
ACTUATORS
SG90 × 2
Sorting + Dispenser servos
DS3218 / NEMA-17
Lifting mechanism
N20 (12V, 400rpm)
Shooting DC motor
L298N H-Bridge
Motor driver module
16×2 I²C LCD
Display & user feedback
Buzzer
Sound feedback
TIMING BUDGET
Sort + classify
0.2 s
Gate reset
0.1 s
Lift to rail
0.4 s
Motor shoot
0.2 s
Motor reset
0.1 s
Total cycle
≤ 2.0 s

## Slide 8
PERFORMANCE SPECIFICATIONS
≥95%
Sorting Accuracy
≥ 19/20 balls correct
≤2.0s
Cycle Time
Detection → Launch
<5cm
Shot Variance
Landing repeatability
<50ms
IR Response
Ball detection latency
Parameter | Value | Notes
Sorting gate precision | ±5° | Rotary gate alignment
Launch velocity | ≈ 2.7 m/s | At 35° launch angle
Lifting peak velocity | 0.5 m/s | Belt drive peak speed
Lifting peak torque | 4.84 N·m | Trapezoidal velocity profile
Footprint | ≤ 600×600 mm | Compact desktop use
System weight | < 1.5 kg | Portability target
Budget | < 5,000 EGP | Prototype cost cap

## Slide 9
INTEGRATION TESTING PLAN
Each subsystem must pass unit tests before full integration proceeds
T1
IR Sensor Detection
✓ Ball detected within 50 ms | Oscilloscope / Serial Monitor
T2
Color Classification
✓ ≥ 19/20 balls correctly sorted | Manual run of 20 balls
T3
Sorting Gate Rotation
✓ Gate reaches ±5° of target | Protractor + servo feedback
T4
Lifting Mechanism
✓ Ball reaches top rail ≤ 0.4 s | Stopwatch timing
T5
Shooting Accuracy
✓ Ball lands within 5 cm of target | 10-shot grouping test
T6
Full Cycle Integration
✓ Cycle ≤ 2.0 s; zero jams | End-to-end timed × 10
T7
Repeated Operation
✓ 50 consecutive cycles OK | Endurance run

## Slide 10
BILL OF MATERIALS
# | Component | Qty | Subsystem | Notes
1 | Arduino Nano | 2 | Control | Master (I²C, BT, LCD) + Slave (lift/shoot/sort)
2 | SG90 Micro Servo | 2 | Sorting + Dispenser | PWM-controlled, 4.9× safety factor
3 | High-Torque Servo / NEMA-17 | 1 | Lifting | DS3218 class or NEMA-17 + driver
4 | N20 DC Gear Motor (12V) | 1 | Shooting | ~400 rpm, stall ≈ 0.025 N·m
5 | L298N H-Bridge Module | 1 | Motor Driver | 12V motor / 5V logic
6 | IR Obstacle Sensors | 5 | Sensing | Dispenser, Box, Shooting, Sort Low/High
7 | Optical Encoder | 1 | Feedback | Speed feedback for PID control
8 | HC-06 Bluetooth Module | 1 | Comms | Wireless PC GUI
9 | 16×2 I²C LCD | 1 | Display | Game prompts & feedback
10 | PLA Filament (~200g) | 1 roll | Structure | Frame, arm, gate, pulleys, balls
11 | 12V Li Battery + Buck Converter | 1 | Power | Dual-rail: 12V motor / 5V logic
Estimated total cost: < 5,000 EGP

## Slide 11
TEAM CONTRIBUTIONS
20%
Ahmed Mohamed Taha
24P0050
Shooting mechanism design, projectile motion calculations, actuator sizing
20%
Nada Abdelhamid
2301102
Lifting mechanism design, GUI development, system integration, LCD programming
20%
Mohamed Samy Taha
24P0373
Software & hardware fabrication, assembly, dispenser mechanism design
20%
Rawaa Tarig Algadi
2101367
PCB design, wiring diagrams & Arduino programming
20%
Farida Mohamed Saeed
24P0008
Sorting mechanism design, Arduino & PID programming, CAD designs & assembly

## Slide 12
CONCLUSION
✅ Successfully integrated mechanical, electrical, and software subsystems into one cohesive mechatronic product
🎮 Interactive color-recognition game demonstrates how mechatronics supports real educational objectives
🔄 Closed-loop PID control + sensor feedback ensures reliable autonomous operation every cycle
📡 Dual Arduino Nano architecture (I²C + Bluetooth) delivers modularity and wireless monitoring
🏗️ Completed within a 5,000 EGP budget using 3D-printed PLA/TPU structure on a 600×600mm base
MCT231 · Ain Shams University · ICHEP · 2025